## Slide 1
Power Prediction and Energy Arbitrage Modeling for Wind Farms Using ML
Date : 06.01.2026
Place: Flensburg
Presented:
Karan Soni
Madhvesh Gorakhiya

## Slide 2
1
Introduction
2
Problem Statement
3
Data & Preprocessing
4
ML Models
6
Flowchart
7
Economic Analysis
8
Results
9
Conclusion
10
Future Tasks
5
Hydrogen Storage Concept
Overview

## Slide 3: 1. Introduction
Wind Energy: One of the fastest‑growing (Germany)
Wind power (variable)  wind speeds (change)
Electricity markets (fluctuate)  Wind production (high)
Modern energy systems increasingly use data and machine learning:
  improve forecasting
  operational decisions
Reference: Statistics Germany | BWE e.V.

## Slide 4: 2. Problem Statements
Wind power output changes every hour → difficult to predict
Electricity prices fluctuate strongly → revenue is uncertain
Selling at the wrong time reduces profit for wind‑farm operators
Hard to know when storing energy will be more profitable than selling
A data‑driven ML model is needed to support STORE vs SELL decisions
Fig 2.1: Day Vs Power generation (MW) (Own).

## Slide 5: 3. Data and Preprocessing
Wind Data (ERA5):
Reference:
Used ERA5 reanalysis dataset for wind components (u100, v100)
Calculated wind speed at 100m
Converted to a clean CSV file (wind_speed.csv)
2. Electricity Price Data:
Reference:
Imported sport market prices (EUR/MW)
Cleaned timestamps and extracted hour and month
3. Power Curve Processing:
Location: Reusenkoog, Germany
Scaled for 51 turbines (total farm capacity) (1)
Used Vestas V112‑3.3 MW turbine power curve (2)
Converted wind speed → power output

## Slide 6: 4. Flowchart
Start
Load wind data, Finding wind speed & Save CSV file
Load market prize data
Compute form power output based on power curve
Apply Polynomial & Linear regression ML models
Evaluate or verification of models
Apply Logistic regression ML model
Verified model
Plot graphs
CSV File
Compare economical model
Create plots
Stop

## Slide 7: 5. Machine Learning Models
Why ML?
Gives a more mathematical and accurate solution
ML helps automate STORE vs SELL decisions
ML learns from historical data and improves decision accuracy
Patterns are non‑linear and difficult to capture manually
1
2
3
4
5
Fast growing and widely used field
Reference: https://www.vecteezy.com/free-photos/machine-learning

## Slide 8: 5. Machine Learning Models
Input
Polynomial & Regression Model
Output
Number of Wind Turbine
Wind speed
Power curve
Evaluate Model
R2
RMSE
MAE
Polynomial and linear trend on hourly based
polynomial and linear trend on days based
No focusing yet
Block Diagram of Wind Farm Model:
Date & time

## Slide 9: 5. Machine Learning Models
Input
Logistic Regression Model
Output
Power (Model 1)
Price
Seasonal Demand Index
Coefficient Interpretation
Decision Plot
(SELL (0) or STORE (1))
No focusing yet
Decision Arbitrage Model:
Season | Months | Factor
Winter | 12, 1, 2 | 1.2
Spring | 3, 4, 5 | 0.9
Summer | 6, 7, 8 | 0.8
Autumn | 9, 10, 11 | 1
Date & time
Store if price < 25
Gives Hours and Days for store energy
Final CSV File
Date
Hour
Power, price
Store decision

## Slide 10: 6. Hydrogen Storage Concept

## Slide 11: 7. Economic analysis

## Slide 12: 8. Results
Polynomial Regression Model:
R2 : 0.14
RMSE : 1155
MAE : 993
Linear Regression Model:
R2 : 0.02
RMSE : 1230
Mae : 1079
Model 1: Polynomial and Regression Model
Fig 8.1: Day Vs Power

## Slide 13: 8. Results
Polynomial Regression Model:
R2 : 0.94
RMSE : 3347
MAE : 2723
Linear Regression Model:
R2 : 0.16
RMSE : 12308
Mae : 10524
Model 1: Polynomial and Regression Model
Fig 8.2: Hours Vs Power

## Slide 14: 8. Results
Polynomial Regression Model:
R2 : 0.94
RMSE : 3347
MAE : 2723
Linear Regression Model:
R2 : 0.16
RMSE : 12308
Mae : 10524
Model 2: Logistic Regression Model
Fig 8.2: Hours Vs Power

## Slide 15: 9. Conclusion

## Slide 16: 10. Future Tasks
Add more feature of wind (air density, wind direction, turbulence)
Improve power curve for better outputs
Try higher order polynomial regression
Use some other ML models
Improve data cleaning
Possible to use more years of data
Add more economic features (forecasted prices, market demand, so on)
Optimize the decision threshold
Use real seasonal power demands data
Reference: Wind Farm Layout Design at NAYXA || We´re Wind Energy Experts

## Slide 17: References
https://www.nsenergybusiness.com/projects/reusenkoge-wind-farm-expansion/?cf-view
https://en.wind-turbine-models.com/turbines/693-vestas-v112-3.3