## Slide 1
Team 5: Power Prediction and Energy Arbitrage Modeling for Wind Farms Using ML
Market Integration and Commercial Optimization, WiSe 2025/26
Presented by: Matriculation No.
Madhvesh Gorakhiya
Soni Karan 760153
Guided by: Prof. Dr. Andreas Heinen
Date : 06.01.2026
Place: Flensburg
GitHub Link: https://github.com/MadhaveshG/wind-h2-arbitrage

## Slide 2
1
Introduction
2
Problem Statement
3
Data & Preprocessing
4
ML Models
6
Flowchart
7
Economic Analysis
8
Results
9
Conclusion
10
Future Tasks
5
Hydrogen Storage Concept
Overview

## Slide 3: 1. Introduction
Wind Energy: One of the fastest‑growing (Germany)
Wind power (variable)  wind speeds (change)
Electricity markets (fluctuate)  Wind production (high)
Modern energy systems increasingly use data and machine learning:
  improve forecasting
  operational decisions
Fig 2.1: Development of wind power supply (6)

## Slide 4: 2. Problem Statements
Wind power output changes every hour → difficult to predict
Electricity prices fluctuate strongly → revenue is uncertain
Selling at the wrong time reduces profit for wind‑farm operators
Hard to know when storing energy will be more profitable than selling
A data‑driven ML model is needed to support STORE vs SELL decisions
Fig 2.1: Day Vs Power generation (MW) (Own).
Research Question:
1. Can machine‑learning models accurately predict wind‑farm power output and identify the optimal hours to STORE or SELL energy?
2. If low‑price energy is stored as hydrogen, can the hybrid system remain economically profitable without subsidies?

## Slide 5: 3. Data and Preprocessing
Wind Data (ERA5):
Used ERA5 reanalysis dataset for wind components (u100, v100) (3)
Calculated wind speed at 100m
Converted to a clean CSV file (wind_speed.csv)
2. Electricity Price Data:
Imported sport market prices (EUR/MW) (5)
Cleaned timestamps and extracted hour and month
3. Power Curve Processing:
Location: Reusenkoog, Germany
Scaled for 51 turbines (total farm capacity) (1)
Used Vestas V112‑3.3 MW turbine power curve (2)
Converted wind speed → power output
4. Electricity Price Data:
Model: 50 MW PEM System (4)
Efficiency: 52.2 kWh /kg H2 Nominal
Min Load: 10% (5MW)

## Slide 6: 4. Flowchart
Start
Load wind data, Finding wind speed & Save CSV file
Load market prize data
Compute form power output based on power curve
Apply Polynomial & Linear regression ML models
Evaluate or verification of models
Apply Logistic regression ML model
Verified model
Plot graphs
CSV File
Compare economical model
Create plots
Stop
GitHub Link: https://github.com/MadhaveshG/wind-h2-arbitrage

## Slide 7: 5. Machine Learning Models
Why ML?
Gives a more mathematical and accurate solution
ML helps automate STORE vs SELL decisions
ML learns from historical data and improves decision accuracy
Patterns are non‑linear and difficult to capture manually
1
2
3
4
5
Fast growing and widely used field
Reference: https://www.vecteezy.com/free-photos/machine-learning

## Slide 8: 5. Machine Learning Models
Input
Polynomial & Regression Model
Output
Number of Wind Turbine
Wind speed
Power curve
Evaluate Model
R2
RMSE
MAE
Polynomial and linear trend on hourly based
polynomial and linear trend on days based
No focusing yet
Block Diagram of Wind Farm Model:
Date & time

## Slide 9: 5. Machine Learning Models
Input
Logistic Regression Model
Output
Power (Model 1)
Price
Seasonal Demand Index
Coefficient Interpretation
Decision Plot
(SELL (0) or STORE (1))
No focusing yet
Decision Arbitrage Model:
Season | Months | Factor
Winter | 12, 1, 2 | 1.2
Spring | 3, 4, 5 | 0.9
Summer | 6, 7, 8 | 0.8
Autumn | 9, 10, 11 | 1
Date & time
Store if price < 25
Gives Hours and Days for store energy
Final CSV File
Date
Hour
Power, price
Store decision

## Slide 10: 6. Hydrogen Storage Concept
Set Economical and Technical Parameters:
H₂ price = 4 (€/kg)
variable O&M = 20% (€/kg)
Electricity Required to produce 1 kg H₂= 52.2 (kWh/kg)
Maximum power capacity of the electrolyze = 50 (MW)
Min load fraction = 10%
Compute Breakeven Electricity Prize:
For Each hour, decide and dispatch:
Store as H₂ :
Sell Electricity:
If store_decision = 1 and (optionally) price ≤ p*:
Run electrolyzer at min(wind, 50 MW) if ≥ 5 MW; else off
H₂ produced = (MW × 1000) / 52.2 kg/h
Electricity sold = wind − electrolyzer_MW
Hybrid net = elec revenue + H₂ revenue − var O&M

## Slide 11: 7. Economic Analysis Modelling
Load: Final_energy_arbitrage_csv
Set Economic Technical Parameters
Input
Compute Breakeven Electricity Prize (
Sell without Storage
Hybrid Model
Compare Strategies
Output
Store Decision Map
Line Plot of Hourly Net
Cumulative Net Over time
Hybrid:
Electricity Revenue
H2 Revenue
OM Cost

## Slide 12: 8. Results
Polynomial Regression Model:
R2 : 0.14
RMSE : 1155
MAE : 993
Linear Regression Model:
R2 : 0.02
RMSE : 1230
Mae : 1079
Model 1: Polynomial and Regression Model
Fig 8.1: Day Vs Power

## Slide 13: 8. Results
Polynomial Regression Model:
R2 : 0.94
RMSE : 3347
MAE : 2723
Linear Regression Model:
R2 : 0.16
RMSE : 12308
Mae : 10524
Model 1: Polynomial and Regression Model
Fig 8.2: Hours Vs Power

## Slide 14: 8. Results
Model 2: Logistic Regression Model
Fig 8.3: Hours Vs Store or Sell Vs Electricity Price

## Slide 15: 8. Results
Model 3: Hydrogen Storage Concepts
Fig 8.4: Store Decision Map

## Slide 16: 8. Results
Model 3: Hydrogen Storage Concepts
Fig 8.5: Hourly Net Value : Without Storage and With Storage

## Slide 17: 8. Results
Model 3: Hydrogen Storage Concepts
Fig 8.6: Cumulative Net Value Over Time

## Slide 18: 9. Conclusion
Improves predicting of wind power output
Optimizing when to sell electricity or store as hydrogen
the current ML model is not fully accurate:
It ignores some additional input variables
Uses only one year of data (2024)
Profitability depends on hydrogen price and system efficiency

## Slide 19: 10. Future Tasks
Add more feature of wind (air density, wind direction, turbulence)
Improve power curve for better outputs
Try higher order polynomial regression
Use some other ML models
Improve data cleaning
Possible to use more years of data
Add more economic features (forecasted prices, market demand, so on)
Optimize the decision threshold
Use real seasonal power demands data
Reference: Wind Farm Layout Design at NAYXA || We´re Wind Energy Experts

## Slide 20: References
https://www.nsenergybusiness.com/projects/reusenkoge-wind-farm-expansion/?cf-view
https://en.wind-turbine-models.com/turbines/693-vestas-v112-3.3
ECMWF. (2024). ERA5 Reanalysis Data. Copernicus Climate Change Service.
Siemens Energy. (2023). Silyzer 300 PEM Electrolyzer Datasheet.
Day-Ahead Auction prices (DE-LU Zone, 2024)
Statistics Germany | BWE e.V.
GitHub Link: https://github.com/MadhaveshG/wind-h2-arbitrage